## Slide 1: Honeywell Ensemble Engine Data Gateway (EDG-100)
Honeywell Confidentiality and IP Notice. The information disclosed by Honeywell on this New Feature Disclosure Form is the confidential and proprietary information of Honeywell International Inc. and is subject to copyright, contractual confidentiality and non-disclosure obligations and the following additional restrictions. The Honeywell intellectual property disclosed herein are Honeywell Core Technologies, are included in Honeywell’s road map and engineering design documentation and may include Honeywell Features, patented technology and patent pending technology. Content must not be disclosed or used by the recipient in pursuit of patents or patent applications. All rights reserved.
EDG-100
Presented to GCC- 11/13
Nazar Janabi

## Slide 2: Honeywell Ensemble- Connected engine
Aircraft Mounted EDG-100
(Honeywell STC)
Press Release (PR)
\
Principles
HTF engine operators currently use a laptop and cable to manually perform engine data download. No modern wireless system available
Business aviation operators using Honeywell’s HTF7K turbofan engines
Via aircraft OEMs and Licensed engine service centers (Channel Partners) using Honeywell STC and PMA
Honeywell EDG-100 Connected Engines Service
Problem
How will it be installed?
Who is it for?
Solution
Description
Improve aircraft engine assurance
Enables advanced analytics/algorithms
Reduces engine maintenance burden/costs
Automated billing
Enables customer savings via Honeywell’s Usage Based MSP program
What is the value?
Aircraft mounted Engine Data Gateway (EDG) Edge node system automates transmitting data wirelessly via wi-fi from engine ECU to Forge and CAMP for Engine Health Monitoring
OEM Value:
Platform modernization
Automation of FAA-required Engine data download
Improve engine assurance
Launch EDG-100 Connected Engines Service in 2024
Notes: Engine Assurance – predictive maintenance before it becomes an operational or safety issue.
Auto Billing – administrative easy
Maintenance Availability – e.g. advance notice of needs to MROs, FOBs, Flight Departments, etc.,

## Slide 3: Honeywell Ensemble architecture
Type of HTF7K Data | ARINC 429 | ECFR RS-422 | RTDL RS-422
Available Data Parameters | ~70 | ~700 | ~90,000
Aircraft Mounted EDG-100
(Honeywell STC)
BA Forge Cloud
Engine Condition Trend Monitoring (ECTM)
Engine Data Viewer (EDV)
in BA Forge
Autonomous
Cessna Longitude with Honeywell HTF7700 Engines
Ground Based
Mobile Device App (CMMA)
RS422 engine data critical for trending
FAA approval received for the STCs. Platforms completed:
Bombardier - Challenger 300/350/3500
Textron - Cessna Longitude
Embraer - Legacy/Praetor

## Slide 4: Data source comparison
Continuously broadcast by engine controller
Parameter list configurable through Honeywell Forge based on algorithm needs
Enables transient trending, LRU monitoring
~25 MB/hr/aircraft
RTDL
(Datalogger)
EDG-100 only
RS422 / ECFR / EEI
ARINC 429
Downloaded from engine controller
Focused on engine maintenance
Includes bin data, event recordings, etc.
Enables snapshot trending, UBMSP
~0.2 MB/month/aircraft
Aircraft bus
Parameters needed for aircraft control
Enables basic trending
~0.5 MB/hr/aircraft
Value for Trending
Snapshots of rich features
~100 params, 10 sets/sec
Subset of params, 1/sec

## Slide 5: Ensemble value evidence
Ensemble Provides Early Warning
Rejected Take Off
Pilot rejected takeoff on the runway because one engine began surging.
Subsequent inspection revealed detached abradable material (used to ensure tight disc-shroud clearance).
Algorithms had been previously developed to identify detached abradable before a compressor surge.
Data received after the event confirmed that the signature of the detached abradable material was present 5 flights before the rejected takeoff.
Had this aircraft been equipped with Honeywell Ensemble, early warning could have been communicated to the operator, enabling them to borescope the compressor, see the missing abradable, and avoid the subsequent event.
Each of the red lines is a trigger from the algorithm

## Slide 6: Key features of EDG-100
Improves access to engine data / Saves customers time and money
Near Realtime access to engine parametric data (including data not available over ARINC429) for prognostic trending.
Enables engine gas path and LRU prognostics to identify issues prior to a flight deck effect in the cockpit, avoiding operational disruption
Connects via Wi-fi. Honeywell recommends pairing device to on-board aircraft wi-fi system
Records real time engine data during flight, but transmits on the ground (only)
STC only
Data meets and exceeds requirements of Honeywell MSP program (ECFR and RTDL files)
Wireless software upload capability
Connects to RS422 port, allowing automatic download of the required engine ECFR snapshot data
Captures timeseries engine data throughout entire flight
Enables recording of any engine ECU software parameter, and over the air updates to parameter list
Cyber Security tested and approved (DAL A Certified)
EDG-100 Edge Node

## Slide 7: Key features of EDG-100
  Specifications​
      Dual Core Processor 1.5 GHz​, 4GB RAM, 64GB eMMC Flash​
      Dual Band Wi-Fi/ Bluetooth​
      RS-232/RS422 Serial Ports​
      Engine Interface Firewall Card (DO-178C DAL A)
      Dedicated TPM 2.0 Module for Security​
      3x Temperature Sensor
      Cloud service hosted on Honeywell Forge
      Engine Data Viewer, Forge web portal for viewing data
      ​Bluetooth Based Mobile App (Android & iOS) to view Real Time Data
      Linux OS
  Operational
      Temp: -40 to 80 c
      Environmental: DO-160G
      Powered by 16 - 32VDC (~300mA)
      Power (Typical) - 8.4W
  Size and Weight
      170 X 80 X 100 (mm) 6.7 x 3.1 x 3.9 (in)
      900 gm (2.0 lbs)
  Secured Engine Data upload @50–100 Mbps
  Engine Real Time Data on Handheld device
6.7 inch (170mm)
Width
3.1 inch (80mm)
Height

## Slide 8
THANK YOU
Aircraft Mounted EDG-100
(Honeywell STC)